HYDRANT ADAPTER WITH CAP

Task Force Tips model #A04EB-ST hydrant adapter and cap shall be provided. For corrosion resistance, the adapter shall be constructed of hardcoat anodized aluminum alloy. The adapter shall comply with NFPA 1963 and 1964 900 PSI hydrostatic testing. The adapter shall be configured with a 4-1/2" female TFT Code EB rigid thread with set screws for anti-tamper feature, and a 5" rigid Storz coupling with lock. A permanently secured 5” Storz cap with lanyard shall be included. Color coded Scotchlite labels shall be included. The unit shall be covered by a five-year warranty.