HYDRANT ADAPTER

Task Force Tips model #A04NR-ST-NC hydrant adapter shall be provided. For corrosion resistance, the adapter shall be constructed of hardcoat anodized aluminum alloy. The adapter shall comply with NFPA 1963 and 1964 900 PSI hydrostatic testing. The adapter shall be configured with a 4-1/2" female NH rigid thread with set screws for anti-tamper feature, and a 5" rigid Storz metal face seal coupling with lock. The unit shall be covered by a five-year warranty.