FORESTRY HOSE CLAMP TOOL

Model # A3095-25. Twenty-five (25) Task Force Tips Forestry Hose Clamps shall be supplied. The hose clamp shall be designed to work on 1” and 1-1/2” (25 and 38 mm) single jacket rubber, canvas, or synthetic jacket hose. The hose clamp shall have a maximum pressure rating of 300 psi (20 bar). A coupling wrench feature shall be included on the upper handle. A gas valve shut off feature shall be included on each side of the hose clamp.

The clamp shall be made of aluminum, stainless steel, and polyurethane. The unit shall be covered by a one-year warranty.