LDH 5-WAY MANIFOLD

A Task Force Tips model # AL92P2P3-SC 5-way manifold shall be provided. The unit shall be configured with a 4" Storz swivel inlet, and 4" Storz swivel outlet with a slow open/close valve with only 2 PSI friction loss at 1000 GPM. The Storz couplings shall be easily configurable to swivel from rigid. The unit shall have four (4) 2-1/2" male NH outlets with slow close aluminum ball valves with full 2-1/2" waterway, and multi-turn knob with valve position indicator. A carrying handle shall be standard. The unit shall be equipped with an automatic pressure relief valve that is adjustable up to 300 psi. A protected pressure gauge shall be included. For corrosion resistance the unit shall be hardcoat anodized aluminum alloy and shall have a silver powder coat interior and exterior finish. Meets NFPA 1964 900 PSI hydrostatic testing. The unit shall have a unique serial number and be covered by a five-year warranty.