JUMBO SIAMESE

Task Force Tips model #AS4ST-ST lightweight aluminum Siamese appliance shall be provided. The appliance shall have a rugged carrying handle, lanyard attachment anchor point and be NFPA compliant with a 900 PSI hydrostatic test rating. Dual clapper valves shall be centrally located at the inlet side of the appliance.

For maximum corrosion protection the aluminum casting shall be hardcoat anodized, with stainless steel components. The appliance shall have a silver powder coat interior and exterior finish.

The appliance shall be configured with two (2) 5" swivel Storz couplings and a 5" swivel Storz coupling and include polymer bearing strips for prevention of galvanic corrosion. The Storz couplings shall be easily configurable as swivel or rigid with a tool. The unit shall have a unique serial number and be covered by a five-year warranty.