SIAMESE APPLIANCE

Task Force Tips model # AS9NJ-ST lightweight aluminum Siamese appliance shall be provided. The appliance shall be NFPA compliant with a 900 PSI hydrostatic test rating. A clapper valve shall be centrally located at the inlet side of the appliance. The unit will have carbide tipped spikes and compatible with Crossfire Safe-Tak portable monitor base with 5” Storz inlet.

For maximum corrosion protection the aluminum casting shall be hardcoat anodized, with stainless steel components. The appliance shall have a red powder coat interior and exterior finish.

The appliance shall be configured with two (2) 2-1/2" female NH swivel rocker lug couplings and a 5" Storz swivel coupling and include polymer bearing strips for prevention of galvanic corrosion. The Storz coupling shall be easily configurable as swivel or rigid with a tool. The unit shall have a unique serial number and be covered by a five-year warranty.