HI-RISE ELBOW WITH PRESSURE GAUGE

A Task Force Tips model # AVG2ENJNJ hi-rise elbow with pressure gauge shall be provided. The lightweight 45 degree elbow shall be configured with a 2-1/2" female NH rocker lug swivel inlet and 2-1/2" male NH rigid outlet. A 3/4" NPT female quarter-turn bleeder valve shall be standard. The pressure gauge shall be liquid filled, have a pressure range of 0-200 PSI (0-14 bar), protected to prevent damage and utilize a pitot type measurement device. The gauge and drain valve portion of the elbow rotate 360 degrees for viewing of the pressure gauge. For corrosion resistance the unit shall be hardcoat anodized and shall have a durable silver powder coat finish. The unit shall have a unique serial number and be covered by a five-year warranty.