HI-RISE ELBOW VALVE WITH PRESSURE GAUGE

A Task Force Tips model # AVGSC2LNJNJ hi-rise elbow slow close valve with pressure gauge shall be provided. The lightweight 45 degree elbow valve shall be configured with a 2-1/2" female NH rocker lug swivel inlet and 2-1/2" male NH rigid outlet. The unit shall have quarter-turn aluminum ball valve with full 2-1/2" waterway, and multi-turn knob with valve position indicator on the left side of the elbow. A 3/4" NPT female quarter-turn bleeder valve shall be standard. The pressure gauge shall be liquid filled, have a pressure range of 0-200 PSI (0-14 bar), protected to prevent damage and utilize a pitot type measurement device. The gauge shall be on the outlet side of the valve. The gauge and drain valve portion of the elbow rotate 360 degrees for viewing of the pressure gauge. For corrosion resistance the unit shall be hardcoat anodized and shall have a durable silver powder coat finish. The unit shall have a unique serial number and be covered by a five-year warranty.