HI-RISE VALVE WITH GAUGE

A Task Force Tips model # AVGSC3SNJNJ slow close ball hi-rise valve with gauge shall be provided. The lightweight valve shall be configured with a 2-1/2" female NH rocker lug swivel inlet and 2-1/2" male NH rigid outlet that pivots 20°. The unit shall have quarter-turn aluminum ball valve with full 2-1/2" waterway, and multi-turn knob with valve position indicator. A 3/4" NPT female plugged bleeder valve port shall be standard. The gauge shall be liquid filled, have a pressure range of 0-300 PSI, protected to prevent damage and utilize a pitot type measurement device. The gauge shall be on the outlet side of the valve. For corrosion resistance the unit shall be hardcoat anodized and shall have a durable silver powder coat interior and exterior finish. The unit shall have a unique serial number and be covered by a five-year warranty.