STANDPIPE GATED WYE

A Task Force Tips model # AYG-NJ-NF gated wye shall be provided. The lightweight wye shall be configured with a 2-1/2" female NH swivel rocker lug inlet and two (2) 1-1/2" male NH outlets. One male outlet shall be provided without a valve for direct connection to the fire hose. This outlet shall have a protected, integral 0-200 PSI pressure gauge. The other outlet shall have a 1/4 turn aluminum ball valve with a Nylon folding handle. For corrosion resistance the valve shall be hard coat anodized and shall have a durable silver powder coat interior and exterior finish. The unit shall have a unique serial number and be covered by a five-year warranty.