LOW PRESSURE AUTOMATIC NOZZLE

Task Force Tips Ultimatic 125, model # BP20-131 automatic nozzle with shutoff shall be provided. The nozzle design shall allow for straight stream through dense wide fog patterns and be able to be flushed without shutting down. For corrosion resistance and durability, the nozzle shall be constructed from hardcoat anodized aluminum alloy, have a six (6) position detent flow control stainless steel slide valve, a protective rubber bumper with fog teeth, stainless steel inlet debris screen, laser engraved serial number, and reflective labeling. An integral blue pistol grip handle shall be positioned directly below the valve handle. A flow detent latch shall limit the valve from opening beyond the 200 LPM mark on the flow label. The flow detent shall have a release lever to allow increased flow.

The stream shaper shall have a detent and tactile indicator when in the flashover stream pattern position.

The nozzle shall have a 1-1/2" female BSP inlet, which allows the nozzle to swivel when tightened, a flow range of 150-400 LPM at 3.5 BAR and be designed to accept the Task Force Tips FJ-U low expansion or FJ-UMX FoamJet multi expansion foam attachments. The nozzle shall have a unique serial number and be covered by a five-year warranty.