DRY CHEMICAL NOZZLE

Task Force Tips model # BTFT-DC5-ND dry chemical nozzle shall be provided. The nozzle shall be designed to deliver dry chemical powder at a rate of five pounds per second. The front portion of the nozzle shall be designed with a straight through path, include straightening fins and withstand the abrasive nature of dry chemical powder. For corrosion resistance and durability the nozzle shall be constructed from hardcoat anodized aluminum alloy, have a six (6) position detent flow control stainless steel slide valve, stainless steel inlet debris screen, laser engraved serial number, and reflective labeling. An integral pistol grip handle shall be positioned directly below the valve handle.

The nozzle shall have a 1" female NH swivel coupling and an effective discharge reach of 75 feet at full flow. The nozzle shall have a unique serial number and be covered by a five-year warranty.