MULTI-THREAT CAB AIR DECONTAMINATION UNIT

Task Force Tips model # CC-021 CrewProtect™ 20 air decontamination system shall be provided. The patent pending multi-stage air decontamination unit shall be compact for mounting in the cab of smaller new and in-service emergency apparatus such as ambulance driving compartments, Chief’s vehicles, wildland trucks, and tiller cabs. The unit shall purify the air by reducing particulates and Volatile Organic Compounds (VOCs). The Crew Protect 20 shall also reduce aerosols carrying viruses and bacteria by over 99%.

The unit can be mounted horizontally, vertically, or inverted using the provided mounting brackets. The system connects to 12 volts DC, only drawing 2 amps, and runs whenever the apparatus is operating. The unit shall have an air flow rate of 20 CFM (0.57 cubic m/min) and operate at 45 decibels, below the NFPA maximum of 90 decibels. The unit shall exchange the air every 3-1/2 minutes in an average small apparatus cab of 65 cubic feet (1.8 cubic meters).

The unit shall be in a protective steel case that is powder coated grey inside and out. The unit shall be 7.25” long, 6” wide and 4” tall (185 x 153 x 102 mm).

A single replacement cartridge element # CC-029 uses RFID technology to assure correct replacement cartridges are installed. Unit will not operate unless correct RFID cartridge is installed, to provide protection for the crew. The current condition of the cartridge is tracked by three LED lights, green, amber, and red, on the prominent face of the unit.

The unit shall have a unique serial number and be covered by a three-year warranty.