MULTI-THREAT CAB AIR DECONTAMINATION UNIT

Task Force Tips model # CC-302 CrewProtect™ 100 air decontamination system shall be provided. The patent pending multi-stage air decontamination unit shall be compact for mounting in the cab of new and in-service emergency apparatus. The unit shall purify the air by reducing particulates and Volatile Organic Compounds (VOCs). The Crew Protect 100 shall also reduce aerosols carrying viruses and bacteria by over 99%.

The unit can be mounted horizontally, vertically, or inverted using the provided mounting brackets. The system connects to 120 volts AC. The unit shall have an air flow rate of 100 CFM (2.83 cubic m/min) and operate at 60.2 decibels, below the NFPA maximum of 90 decibels. The unit shall exchange the air every 3-1/2 minutes in an average apparatus cab of 350 cubic feet (9.9 cubic meters).

The unit shall be in a protective steel case that is powder coated charcoal grey inside and out. The unit shall be 20” long, 12” wide and 4-1/2” tall (508 x 305 x 115 mm).

A single replacement cartridge element # CC-305 uses RFID technology to assure correct replacement cartridges are installed. Unit will not operate unless correct RFID cartridge is installed, to provide protection for the crew. The current condition of the cartridge is tracked by three LED lights, green, amber, and red, on the prominent face of the unit.

The unit shall have a unique serial number and be covered by a three-year warranty.