BLUETOOTH® IN-LINE FLOW METER

Task Force Tips model # EFF-BFBF125 SHO-FLOW® 1 Bluetooth® flow meter shall be provided. The inline flow meter shall have a flow range of 25-125 gpm (100-500 l/min). The unit shall be self-powered and transmit a Bluetooth® signal to any Android* or Apple® smart device via Task Force Tips downloadable app. The unit shall be self-powered by means of an internal water turbine and shall require no batteries or wires to operate. The unit shall report flow in real time in gpm, gps, lpm, or lps and shall have a resettable totalizer feature in the app. The unit shall have 1-1/2” female BSP rocker lug swivel inlet and 1-1/2” male BSP rigid outlet. The flow meter shall have a unique serial number and be covered by a 5-year warranty.

*Android is a trademark of Google LLC.