IN-LINE BLUETOOTH® IN-LINE FLOW METER

Task Force Tips model # EFF-SHSH300 SHO-FLOW® 1 Bluetooth® flow meter shall be provided. The inline flow meter shall have a flow range of 50-300 gpm (200-1150 l/min). The unit shall be self-powered and transmit a Bluetooth® signal to any Android or Apple smart device via Task Force Tips downloadable app. The unit shall be self-powered by means of an internal water turbine and shall require no batteries or wires to operate. The unit shall report flow in real time in gpm, gps, lpm, or lps and shall have a resettable totalizer feature in the app. The unit shall have 52mm Storz inlet and 52mm Storz outlet. The flow meter shall have a unique serial number and be covered by a 5-year warranty.