BLUETOOTH® PRESSURE GAUGE

Task Force Tips model # EPG300 Bluetooth pressure gauge shall be provided. The gauge shall transmit a Bluetooth signal to any Android* or Apple® smart device via Task Force Tips downloadable app. The unit shall report pressure in real time in psi, bar, or kPa. The unit shall have a pressure range of 0-300 PSI (0-21 bar), and include a protective cover to prevent damage. The gauge shall thread into a 1/4” female NPT port and read pressure of the device it is installed in.

The gauge shall be configured with a 1/4” male NPT inlet. The unit shall be covered by a five-year warranty.