NOZZLE SHUTOFF

Task Force Tips model # F140F ball valve shutoff shall be supplied. For corrosion resistance, the valve body shall be constructed from hardcoat anodized aluminum extruded alloy and include a quick-change rear valve seat and stainless steel shut off ball. The waterway shall have a 1-3/8" diameter unobstructed path and comply with the current NFPA 1964 Standard.

The valve operating handle shall be made of glass-filled Nylon and be attached to the stainless steel ball with a stainless steel trunnion threaded through then handle and into the ball on each side. A stainless steel roll pin shall secure the handle to the trunnion on each side. The couplings shall be configured as a 1-1/2" female NH rocker lug swivel inlet and a 1-1/2" male NH outlet and be suitable for use with smooth bore tip, stack tip, or combination fog/straight stream nozzles or used for break-and-extend operations. The unit shall have a unique serial number and be covered by a five-year warranty.