DUAL GALLONAGE ELECTRIC REMOTE FOAM NOZZLE

Task Force Tips model # F2060BCER Bubble Cup dual gallonage foam nozzle with electric pattern and flow control shall be supplied. The nozzle shall be capable of producing either a fog or straight stream with the ability to instantly aspirate foam by sliding a sleeve forward. For corrosion resistance the nozzle shall be constructed from hardcoat anodized aluminum.

The electric drive unit be enclosed in a waterproof housing and include a manual override device in the event the power source fails. The unit shall be compatible with 12 or 24-volt power systems and require no more than a 5-amp peak and 3-amp nominal current draw and include a waterproof connection cable with plug. Nozzle stream shaper actuator shall have position encoder for smooth transition between off, straight stream and fog patterns with fine stream adjustment. Electrical actuator systems shall have a rating of IP66/IP67 per IEC 65029.

The nozzle shall be configured for flow settings of 20 and 60 GPM at 100 PSI, have a 1-1/2" female NH swivel rocker lug inlet and have an off position for shut off of the water flow. The unit shall have a unique serial number and be covered by a written five-year warranty.