LOW EXPANSION FOAM ATTACHMENT

Task Force Tips model # FJ-LX-M3 FoamJet air aspirating tube attachment for low expansion foam production shall be provided. The device shall be designed for use with Task Force Tips Master Stream large body 1250 series and 1500 series nozzles. The FoamJet shall be constructed from molded polymer, Nylon, and hardcoat anodized aluminum. The attachment shall be able to produce a quality foam blanket using most commonly used concentrates and be able to be quickly removed to restore the nozzle to its original configuration. The unit shall have a unique serial number and be covered by a five-year warranty.