MULTI EXPANSION FOAM ATTACHMENT

Task Force Tips model # FJ-MX-FQ FoamJet air aspirating attachment for multi expansion foam production shall be provided. The device shall be designed for use on TFT 1-1/2" Quadrafog series nozzles with flow rates of 30-125 GPM and constructed from molded polymer, Nylon, and hardcoat anodized aluminum. The attachment shall be able to produce a quality foam blanket using most commonly used concentrates and be able to be quickly removed to restore the nozzle to its original configuration. The unit shall have a unique serial number and be covered by a five-year warranty.