SELECTABLE GALLONAGE NOZZLE

Task Force Tips Thunder Fog, model # FTS-EWPS-BIC selectable gallonage nozzle with shutoff shall be provided. The nozzle design shall allow for straight stream through wide fog patterns with user selectable flows and be able to be flushed without shutting down. For corrosion resistance and durability, the nozzle shall be constructed from hardcoat anodized aluminum alloy, have a stainless steel ball valve with polymer valve seat, a protective rubber bumper, stainless steel spinning fog teeth, laser engraved serial number, reflective labeling and five year warranty. An integral pistol grip handle shall be positioned directly below the valve handle.

The nozzle shall have six (6) selectable flow settings @ 7 bar:

110 l/min

230 l/min

360 l/min

470 l/min

570 l/min

750 l/min

The nozzle shall have a 2-1/2" male BIC swivel inlet, which allows the nozzle to swivel when tightened and be designed to accept the Task Force Tips FJ-MX-FT FoamJet multi expansion foam attachment.