NOZZLE SHUTOFF

Task Force Tips model # H-2VO ball valve shutoff shall be supplied. The shutoff shall be designed with a six (6) position detent (click stop) flow control handle. For corrosion resistance, the valve body shall be constructed from hardcoat anodized aluminum extruded alloy and have a Nylon shut off ball. The waterway shall have a 1-3/8" diameter unobstructed path and comply with the current NFPA 1964 Standard.

The couplings shall be configured as a 2-1/2" female NH rocker lug swivel inlet with the ability to continuously swivel when tightened and a 1-1/2" male NH outlet and be suitable for use with smooth bore tip, stack tip, or combination fog/straight stream nozzles or used for break-and-extend operations. The unit shall have a unique serial number and be covered by a five-year warranty.