PLAYPIPE WITH SHUTOFF

Task Force Tips model # H-2VPP playpipe with shutoff valve shall be provided. For corrosion resistance the valve body shall be constructed from hardcoat anodized aluminum extruded alloy and have a Nylon shut off ball. The playpipe shall have rubber coated wrap around handles to allow for reduced fatigue and a better grip during wet and cold weather operations. The shutoff shall be designed with a six (6) position detent (click stop) flow control handle.

The couplings shall be configured as a 2-1/2" female NH swivel with the ability to continuously swivel when tightened and a 1-1/2" male NH and be suitable for use with smooth bore tip, stack tip, or combination fog/straight stream nozzles or used for break-and-extend operations. The unit shall be covered by a five-year warranty.