BLUETOOTH® IN-LINE PRESSURE GAUGE

Task Force Tips model # J25G300BS Bluetooth in-line pressure gauge with pivoting outlet shall be provided. For corrosion resistance the body shall be constructed from hardcoat anodized and powder coated aluminum alloy. The gauge shall transmit a Bluetooth signal to any Android* or Apple® smart device via Task Force Tips downloadable app. The unit shall report pressure in real time in psi, bar, or kPa. The unit shall have a pressure range of 0-300 PSI (0-21 bar) and include a protective cover to prevent damage. The gauge shall read sidewall pressure.

The gauge shall be configured with a 2-1/2" female NH swivel rocker lug inlet and a 2-1/2" male NH rigid outlet that pivots 40° to reduce hose kinking. The unit shall have a unique serial number and be covered by a five-year warranty.