SELECTABLE GALLONAGE NOZZLE

Task Force Tips QuadraFog, model # QF1000SL selectable gallonage nozzle with shutoff shall be provided. The nozzle design shall allow for straight stream through wide fog patterns with user selectable flows and be able to be flushed without shutting down. For corrosion resistance and durability, the nozzle shall be constructed from hardcoat anodized aluminum alloy, have a stainless-steel ball valve, a protective rubber bumper, fixed fog teeth, laser engraved serial number, reflective labeling and five-year warranty. An integral pistol grip handle shall be positioned directly below the valve handle. The nozzle shall comply with the current EN15182-2 Type 3 standard.

The nozzle shall have five (5) selectable flow settings @ 6 BAR:

285 L/MIN

500 L/MIN

600 L/MIN

800 L/MIN

1000 L/MIN

The nozzle shall have a 75 mm Storz swivel inlet and be designed to accept the Task Force Tips FJ-MX-FT FoamJet multi expansion foam attachment.