REMOTE ELECTRIC DISPERSED PATTERN NOZZLE

Task Force Tips Model Number SVXE Vortex 6 nozzle with electrically controlled pattern control shall be provided. Water dispersion will be consistent throughout the Vortex pattern and will not affect the water flow volume. Angle of dispersion can be adjusted from 0-30 degrees.  Full range angle change activation is less than 12 seconds.

The electric drive unit be enclosed in a waterproof housing and include a manual override device in the event the power source fails. The unit shall be compatible with 12 or 24-volt power systems and require no more than a 5-amp peak and 3-amp nominal current draw and include a waterproof connection cable with plug. Nozzle stream shaper actuator shall have position encoder for smooth transition between straight stream and dispersed pattern with fine stream adjustment. Electrical actuator systems shall have a rating of IP66/IP67 per IEC 65029.

For corrosion resistance the unit shall be constructed from hardcoat anodized aluminum alloy with stainless steel hardware. Unit shall have a laser engraved serial number and be covered by a five-year warranty.

The couplings shall be configured as a 6" female NH rigid rocker lug coupling and a 6" male NH outlet thread. Unit shall be used with Task Force Tips YST-8 series stacked tip.  Overall length of 11".