PORTABLE FOAM SYSTEM

Task Force Tips model # UM12 PRO/pak portable Class A or B foam delivery system shall be provided. The system shall be constructed of a high impact 2-1/2 gallon plastic tank with a built in eductor made of hardcoat anodized aluminum alloy and stainless steel. The large fill port on the foam tank shall have a built in indicator to display the type of concentrate stored inside the tank as well as a screen to filter out impurities in the foam concentrate.

The container shall have an integral handle, which also functions as a twist grip flow control valve. The unit shall operate with inlet pressures from 40-500 PSI and a nominal flow of 12 GPM at 100 PSI. A field changeable percentage knob shall provide selectable proportioning ratios of one, three and six percent. The unit shall have the operation instructions permanently applied to the unit and have a laser engraved serial number.

The unit shall be supplied with three quick connect nozzles; straight stream, low expansion and medium expansion. A 2.7 foot hose, cap and shoulder strap shall also be supplied. The inlet for the unit shall be configured with a 1" female NH swivel coupling.