FIXED GALLONAGE NOZZLE WITH PRESSURE RELIEF

Task Force Tips Working Fire, model # WF1GFS-226 fixed gallonage nozzle with pressure relief shall be provided. The nozzle design shall allow for straight stream through wide fog patterns, and be able to be flushed without shutting down. A visual and tactile indicator and detent for straight stream position shall be standard. Tactile indicator ring shall be black (standard), or can be specified in optional colors of blue, red, or yellow. For corrosion resistance and durability, the nozzle shall be constructed from hardcoat anodized aluminum alloy, have a stainless steel ball valve, a rubber bumper, stainless steel spinning fog teeth, and reflective labeling. An integral pistol grip handle shall be positioned directly below the valve. The valve handle covers and pistol grip shall be black (standard), or can be specified in optional colors. Valve handle opening is 3-1/2” wide by 1-1/2” tall and designed to accommodate folded hose.

The nozzle shall flow 160 GPM at 50 PSI. The nozzle shall have the capability to increase flow above 160 gpm while relieving excess nozzle pressure. The increase in nozzle reaction forces shall be directly proportional to the increase in flow.

The nozzle shall have a 1-1/2" female NH swivel rocker lug inlet that allows the nozzle to swivel when tightened and be designed to accept the Task Force Tips FJ-LX-HM low expansion or FJ-MX-HM medium expansion foam attachments. The unit shall be covered by a five-year warranty.