MONITOR EXTENSION PIPE

Task Force Tips model # XG18XL-XL extension pipe shall be provided. The user installed extension pipe shall allow the truck mounted Task Force Tips Crossfire monitor to be raised 15-3/4” while maintaining the ability to horizontally rotate the monitor device 360 degrees.

The aluminum extension pipe shall have a 3" waterway; hardcoat anodized finish and be furnished with a Task Force Tips Crossfire female quick connect inlet with locking pawls and a Crossfire quick connect male outlet. The unit shall have a unique serial number and be covered by a five-year warranty.