PORTABLE ATTACK MONITOR

Task Force Tips Blitztac model # XXB141A portable lightweight attack monitor shall be supplied.

The monitor shall include an integral safety gating device that will automatically reduce the water flow in the event the monitor slides or lifts. The safety gating device can be easily reset. The water flow is controlled by a valve with a positive lock in the “off” position to prevent accidental discharge of the stream.

The water inlet shall pivot up and down to allow a smooth transition from the hose to the monitor for increased stability. The discharge has vertical elevation travel between 25 and 50 degrees unassisted and down to 10 degrees when assisted, above horizontal with a ball and socket joint. The same ball and socket joint shall allow for horizontal adjustment of 20 degrees left and right of center. The discharge outlet shall have a removable stream straightener.

The monitor shall have folding stabilization legs with carbide tips, which are concealed in the carry and stow positions. An integral carrying handle that also functions as an attachment point for the included anchor strap with attached storage bag shall be provided. For corrosion resistance, the monitor shall be constructed from hardcoat anodized aluminum alloy and have a blue powder coat interior and exterior finish.

The monitor shall be configured with a 2-1/2” male BIC inlet and 2-1/2" male NH rigid outlet with a flow rating up to 500 GPM. The unit shall have a unique serial number and be covered by a five-year warranty.