2000 GPM FIXED LOCATION MONITOR

Task Force Tips Monsoon, model # Y4-T21A-Z manually controlled monitor shall be provided. The monitor shall operate with an aluminum crank which controls a stainless steel worm gear for elevation adjustment and a long tiller bar for rotation adjustment and include a locking knob.

The monitor shall have the following capabilities:

- Full horizontal rotation with continuous 360-degree travel;

- 135 degrees of vertical travel from 45 degrees below and 90 degrees above horizontal;

- Field changeable elevation stops at 30 and 45 degrees above horizontal and 30 degrees below horizontal;

- Field changeable rotation stops shall be provided at 45, 90 and 135 degrees left and/or right of center;

- Flow capability of 2000 GPM with a friction loss of no more than 16 PSI;

- Maximum operating pressure of 200 PSI.

For resistance to corrosion the monitor shall be constructed from hardcoat anodized aluminum with an American red powder coat interior and exterior finish. A threaded port for an optional pressure gauge shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty. Monitor shall be FM approved.

The monitor shall be designed with a unique waterway that minimizes the path of travel, reduces friction loss and turbulence, and produces a far reaching water stream. The monitor shall be configured with a 4" ANSI 150 flange inlet and 3-1/2" male NH outlet.