1500 GPM REMOTE CONTROLLED AERIAL LADDER MONITOR

Task Force Tips Typhoon RC, model # Y5-E21A-L-03 remote controlled aerial ladder monitor shall be installed. The monitor shall operate on 12 or 24 volt direct current and controlled by a monitor mounted operator station with functions that control rotation, elevation, nozzle patterns, programmable park and oscillate, auxiliary 1 and auxiliary 2. The monitor shall be compatible with optional wired and wireless control stations and monitor position display.

The electrical controls for the monitor shall be waterproof and utilize current limiting and position encoders to protect the drive train at the ends of travel. A six-pin electrical connection for a TFT remote control nozzle shall be provided. Electrical enclosure systems on the monitor shall have a rating of IP66/IP67 per IEC 65029. The monitor shall be equipped with small override knobs for use in the event of power failure or electrical malfunction. The motors and knobs control stainless steel worm gears for rotation and elevation adjustment.

The monitor shall have the following capabilities:

- Control box mounted to monitor for maximum clearance;

- Override control shafts shall be short in length with small override knobs to provide maximum clearance;

- Electronic park position “stay” feature when monitor is powered;

- Anti-back drive mechanism to maintain monitor position during travel;

- Horizontal stops preset to 90 degrees left and right of center;

- 135 degrees of vertical travel from 90 degrees above horizontal to 45 degrees below horizontal;

- Field changeable stops in 10 degree increments left and/or right and above and/or below horizontal;

- Flow capability of 1500 GPM with 19 PSI of loss;

- Maximum operating pressure of 200 PSI

For resistance to corrosion the monitor shall be constructed from hardcoat anodized aluminum with a silver powder coat interior and exterior finish. The discharge elbow shall include an integral stream straightener. A threaded port for an optional pressure gauge shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty.

The monitor shall be configured with a longer 4" ANSI 150 flange inlet and 3-1/2" male NH outlet.