OPTIONAL REMOTE MONITOR AUXILIARY RELAY INTERFACE BOX

Task Force Tips model # YE-REMAUX auxiliary relay interface box for Monsoon, Hurricane, Typhoon, Tsunami, EF1, and Tornado series remote control monitors shall be installed. The interface box shall allow utilization of the AUX1 and AUX2 buttons located on the monitor operator station, any remote operator station with a membrane switch, or inputs located in model #Y4E-COMM. The interface box shall be equipped with two relays that can operate lights, interface to a valve controller or operate a valve directly. The contact rating of the relay shall be 16 amps @ 30VDC for resistive loads and 8 amps @ 30VDC for inductive loads.

The enclosure shall be weatherproof and utilize weatherproof components such as a silicone seal, hardware with o-rings and liquid tight electrical connections with strain relief fittings. A preconnected 10 foot, four conductor cable for power and communications shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty.