HIGH FLOW STACK TIP SET

Task Force Tips model # YST-8NX smooth bore stacked tip set shall be provided. For corrosion resistance the tip set shall be constructed from hardcoat anodized aluminum alloy. The set shall consist of four (4) tips with the base section having a Task Force Tips proprietary quick connect inlet to attach to Tsunami monitor outlet and have internal stream straightener insert, intermediate section and 3-1/2" outlet tip. The other intermediate tip sizes shall be 4", 4-1/2" and 5-1/8". Each tip shall be labeled with a flow/pressure chart, and orifice size. The unit shall be covered by a five-year warranty.